## Slide 1
Results of the railway traffic survey (May-July 2013)
            EMAH Eco-mobility in the Austro-Hungarian border region
            Álmos VIRÁG, project leader
            Endréné TREPPER, senior researcher
            Viktor SERBÁN, junior researcher
            András NÉMETH, intern

## Slide 2
Railway line no. | Surveyed section | Survey time | 
 |  | WEEKDAY (Friday & Tuesday) | WEEKEND (Sunday)
512 | Deutschkreutz – Sopron – Neufeld / Leitha | 5:14 - 9:52 | -
 |  | 13:37 - 19:52 | 13:37 - 20:52
524 | Deutschkreutz – Sopron – Wiener Neustadt | 4:46 - 10:42 | -
 |  | 13:47 - 20:18 | 14:46 - 20:42
530 | Szentgotthárd – Fehring – Feldbach | 6:19 - 9:47 | -
 |  | 13:00 - 20:02 | 14:06 - 21:47
700 | Győr - Hegyeshalom – Bruck / Leitha | 4:48 - 10:10 | -
 |  | 13:48 - 21:10 | 13:48 - 21:10
731 | Fertőszentm. – Pamhagen – Bad Neusiedl / See | 6:44 - 8:42 | -
 |  | 12:19 - 17:15 | 12:19 - 17:15
Survey characteristics

## Slide 3
524 [Wien –] Wiener Neustadt – Sopron – Deutschkreutz
Wr. Neustadt – Deutschkreutz
Deutschkreutz – Wr. Neustadt
Part of the suburban traffic of Wien (and Wiener Neustadt): - monotonous decreasing traffic volume towards Austro-Hungarian border
Sopron is the 2nd busiest train station
Mattersburg: minor centre in Burgenland

## Slide 4
512 Wien – Ebenfurth – Sopron – Deutschkreutz
Ebenfurth – Deutschkreutz
Deutschkreutz – Ebenfurth
Part of the suburban traffic of Wien: - monotonous decreasing traffic volume towards Austro-Hungarian border
Deutschkreutz: similar traffic volume with Sopron
Wulkaprodersdorf: traffic junction (change towards Eisenstadt)

## Slide 5
700 Wien – Bruck an der Leitha – Hegyeshalom – Győr
Bruck/L. – Mosonmagyaróvár
Mosonmagyaróvár – Bruck/L.
Part of the suburban traffic of Wien - and also Győr: - slightly decreasing traffic volume towards the border (from both ways!)
Hegyeshalom: bigger passenger traffic, partly due to the changes between suburban trains
Parndorf: minor centre (many jobs)

## Slide 6
530 [Graz –] Fehring – Szentgotthárd
Fehring – Szentgotthárd
Szentgotthárd – Fehring
Slightly reducing traffic volume towards Austro-Hungarian border
Fehring: traffic junction (change to Graz, Hartberg and to Wr. Neustadt)
Presently negligible role of suburban traffic of Graz (that is more important from Fehring)

## Slide 7
731 [Wien –] Neusiedl am See – Pamhagen – Fertőszentmiklós
Austrian part: role of suburban traffic of Wien (and Neusiedl am See): - strongly decreasing traffic volume towards the Austro-Hungarian border
- usually less than 10% (!) across the border
At present, cross-border traffic has minor role
Bad Neusiedl am See – Fertőszentmiklós
Fertőszentmiklós – Bad Neusiedl am See

## Slide 8
Comparison of the results of cross-sectional traffic count (May and July 2013)
Cross-border train traffic survey |  |  |  |  | 
 | Investigated trains [pc.] | Passengers [pers.] |  | Cross-border travellers [pers.] | 
24.05. (Friday) | 94 | 7113 |  | 2514 | 
26.05. (Sunday) | 39 | 2151 |  | 657 | 
28.05. (Tuesday) | 97 | 7344 |  | 2741 | 
SPRING TOTAL | 230 | 16608 |  | 5912 | 
12.07. (Friday) | 95 | 6462 | -9,15% | 2582 | 2,70%
14.07. (Sunday) | 36 | 1840 | -14,46% | 662 | 0,76%
16.07. (Tuesday) | 96 | 6785 | -7,61% | 2405 | -12,26%
SUMMER TOTAL | 227 | 15087 | -9,16% | 5649 | -4,45%

## Slide 9
Changes in passenger numbers
 |  | Investi-gated trains [pc.] |  | Passengers total [pers.] | Avg. number of boardings per train [pers.] |  | Cross-border travellers total [pers.] | Avg. number of cross-border travellers p. train [pers.] |  | Rate of cross-border travellers
524 | MAY | 83 |  | 5604 | 68 |  | 2260 | 27 |  | 40%
 | JULY | 92 |  | 6346 | 69 |  | 2224 | 24 |  | 35%
 | DIFFERENCE |  |  | 13% | 2% |  | -2% | -11% |  | -5%
512 | MAY | 51 |  | 4067 | 80 |  | 1591 | 31 |  | 39%
 | JULY | 57 |  | 4067 | 71 |  | 1692 | 30 |  | 42%
 | DIFFERENCE |  |  | 0% | -11% |  | 6% | -5% |  | 3%
700 | MAY | 38 |  | 4698 | 124 |  | 1570 | 41 |  | 33%
 | JULY | 38 |  | 3963 | 104 |  | 1422 | 37 |  | 36%
 | DIFFERENCE |  |  | -16% | -16% |  | -9% | -9% |  | 3%
530 | MAY | 42 |  | 1098 | 26 |  | 387 | 9 |  | 35%
 | JULY | 40 |  | 752 | 19 |  | 371 | 9 |  | 49%
 | DIFFERENCE |  |  | -32% | -28% |  | -4% | 1% |  | 14%

## Slide 10
Results of the survey of travel behaviour

## Slide 11
General information
Number of interviewed passengers |  |  |  |  |  |  |  |  |  |  |  | 
Line | Friday (24 May) | Sunday (26 May) | Tuesday (28 May) | Σ | Sampling rate |  | Line | Friday (12 July) | Sunday (14 July) | Tuesday (16 July) | Σ | Sampling rate
512 | 153 | 43 | 235 | 431 | 11% |  | 512 | 144 | 40 | 174 | 358 | 9%
524 | 232 | 55 | 316 | 603 | 11% |  | 524 | 281 | 66 | 247 | 594 | 9%
530 | 113 | 65 | 98 | 276 | 25% |  | 530 | 76 | 55 | 64 | 195 | 26%
700 | 144 | 67 | 92 | 303 | 6% |  | 700 | 107 | 51 | 86 | 244 | 6%
731 | 19 | 12 | 13 | 44 | 4% |  | - | - | - | - | - | -
Σ | 661 | 242 | 754 | 1657 | 10% |  | Σ | 608 | 212 | 571 | 1391 | 9%
Number of interviewed CROSS-BORDER passengers |  |  |  |  |  |  |  |  |  |  |  | 
Line | Friday (24 May) | Sunday (26 May) | Tuesday (28 May) | Σ | Sampling rate |  | Line | Friday (12 July) | Sunday (14 July) | Tuesday (16 July) | Σ | Sampling rate
512 | 120 | 40 | 204 | 364 | 23% |  | 512 | 129 | 25 | 156 | 310 | 18%
524 | 197 | 43 | 229 | 469 | 21% |  | 524 | 260 | 64 | 240 | 564 | 25%
530 | 79 | 56 | 70 | 205 | 53% |  | 530 | 76 | 55 | 64 | 195 | 53%
700 | 109 | 33 | 72 | 214 | 14% |  | 700 | 106 | 50 | 86 | 242 | 18%
731 | 9 | 2 | 9 | 20 | 19% |  | - | - | - | - | - | -
Σ | 514 | 174 | 584 | 1272 | 22% |  | Σ | 571 | 194 | 546 | 1311 | 23%

## Slide 12
Reason of travel
School-related travels decrease significantly
Major increase in tourism/free time activity and visits
Slight changes in healthcare, administration, work-related travels
(May 2013)
(July 2013)

## Slide 13
Status of passengers
Share of students disappearing  bigger proportion of workers
„Others” increasing: probably more pensioners (relation with the purposes of travel)
(May 2013)
(July 2013)

## Slide 14
Access to car
Sample: daily commuters
Rate of passengers without car access reduced (less students)
CAR AVAILABILITY | answers | percent | answers | percent
YES | 448 | 54,4% | 442 | 64,1%
NO | 318 | 38,6% | 235 | 34,1%
no answer | 57 | 6,9% | 13 | 1,9%
TOTAL | 823 |  | 690 | 
(May 2013)
(July 2013)

## Slide 15
Reasons of using public transport (train) service
Very similar distribution compared with the results of the spring survey
Passengers with car access replied similarly
Most important factors: (reasonable) price, (better) comfort, effective time-spending
Eco-friendliness was considered to be more important by passengers with car access
(July 2013)
(July 2013)

## Slide 16
Overall satisfaction with train schedule:
Some recommendations…
  Generally: more frequent trains, less delays, improved comfort, Wi-Fi, snack/coffee machine, cleaner stations and restrooms, more information (especially on Internet), better connections with public transport
  512: more frequent trains in the evening (off-peak, especially on Saturdays)
  524: REX to Wien at 8:00; other trains with larger capacity
  530: fewer stops to Graz
  700: direct trains again (between Wien and Győr)
SATISFACTION WITH THE CURRENT TIMETABLE | responses | Percent
YES | 600 | 72,9%
NO | 221 | 26,9%
No answer | 2 | 0,2%
TOTAL | 823 | 100,0%
Overall satisfaction, main remarks

## Slide 17
Thanks for your attention!
Questions?